## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2016
Lecture 30:
Continue with PIC example programs:
Interrupts

## Slide 2: Lecture outline
Announcements/reminders
  HW 8: Working with PICkits—groups of up to 4 (3 preferred)
    Due 12/9 by 2:30 PM
  HW 9 to be posted; also due 12/9 by 2:30 PM
    Individual problem set
Review: Timer module
Today’s lecture: interrupts

## Slide 3: Review: clock sources

## Slide 4: Review: Timer module
Internal timers common in microcontrollers
Used to generate delays, measure time between events, or count event occurrences
Typical interrupts for
  Timer overflow (common for generating delay)
  Timer compare (also for generating delay—stop when timer reaches certain value)
  Capture (what value does timer have when event occurs?)
Typical timer configurations
  Run at particular speed relative to system clock (prescaled)
  Increment every time external event occurs
PIC 16F1829 has 5 timers (four 8 bit, one 16 bit)

## Slide 5: Rotate with timer-based delay (asm) (1/2)
Start:
;Setup main init
banksel OSCCON ;bank1
movlw b'00111000’ ;set cpu clock speed to 500KHz
movwf OSCCON
;Configure the LEDs
banksel TRISC ;bank1
clrf TRISC ;make all of PORTC an output
banksel LATC ;bank2
movlw b'00001000‘ ;start with DS4 lit
movwf LATC
;Setup Timer0
banksel OPTION_REG ;bank1
;1:256 prescaler for a delay of:
; (insruction-cycle * 256-counts)*prescaler =
; ((8uS * 256)*256) =~ 524mS
movlw b'00000111’
movwf OPTION_REG

## Slide 6: Rotate with timer-based delay (asm) (2/2)
MainLoop:
btfss INTCON, TMR0IF ;did TMR0 roll over yet?
bra $-1 ;wait until TMR0 overflows
bcf INTCON, TMR0IF ;clear flag in software
;rotate the LEDs
banksel LATC ;bank2
lsrf LATC, f
btfsc STATUS,C ;did bit rotate into carry?
bsf LATC,3 ;yes, light DS4 back up
bra MainLoop ;continue forever
end

## Slide 7: Rotate with timer-based delay (C)
void main(void) {
OSCCON = 0b00111000; //500KHz clock speed
TRISC = 0; //all LED pins are outputs
LATC = 0;
//1:256 prescaler for a delay of: (instruction-cycle * 256
// counts)*prescaler = ((8uS * 256)*256) =~ 524mS
OPTION_REG = 0b00000111;
LATCbits.LATC4 = 1; //start with DS4 lit
while (1) {
//PIC can do work here, but this program just waits for flag
while (!INTCONbits.TMR0IF) continue;
INTCONbits.T0IF = 0; //flag MUST be cleared in software
LATC >> = 1; //rotate the LEDs
if (STATUSbits.C) //when last LED is lit, restart pattern
LATCbits.LATC3 = 1;
}
}

## Slide 8: Exceptions
Exception: unexpected event altering normal program flow
  Often result of an error
  Can occur in HW or SW
    HW exceptions often handled by OS
    Will signal running program to stop
  Examples: divide by 0, system reset, invalid address accessed, breakpoint
  Some programming languages (Java, C++, C#) have software exceptions for program-related events
    Application-level try/catch blocks—attempt code that may fail and “catch” exception if that occurs
  Exceptions are typically synchronous events
    Occur in the course of executing a single instruction

## Slide 9: Interrupts
Interrupt: CPU signal that external event has occurred
  Usually generated by external hardware
    Signals processor to interact with peripheral
    Example: key pressed on keyboard, printer reading from memory, timer completing
  Can be generated by specific instructions
    x86 INT, INTO, BOUND instructions
  Interrupts sometimes seen as subset of exceptions
Interrupts typically asynchronous events
  HW signals can be generated at any time
  Current instruction completes before interrupt is handled

## Slide 10: Interrupt timeline
Shows time dedicated to two potential recurring interrupts + main program
Interrupt service routines (ISRs) kept relatively short
  Functions used to handle interrupts

## Slide 11: General interrupt processing
Decide whether or not to service
  Steps for doing so are processor-dependent
If servicing:
  Complete current instruction
  Save PC (or IP)
    Need to know where to return after servicing interrupt
    ISR is like a function, but you don’t explicitly call it
  Save processor state
    Registers, condition codes
  Jump to start of ISR
  Actually handle interrupt
  Return from interrupt

## Slide 12: Vectors
Interrupt/exception vector: starting address of service routine
Typically stored in vector table
  Often in lowest memory range (start at address 0)
  Some vectors dedicated to specific exceptions/interrupts
    Depends on complexity of processor
    Examples: divide by 0, page fault, alignment error
  Range allowed for user-defined interrupts as well

## Slide 13: PIC Interrupts
PIC controllers allow both internal and external interrupts
Single interrupt service routine
  Must determine interrupt cause, then handle
  Code addresses handled slightly differently
    Processor goes to address 0 on reset, 4 on interrupt
    Reset “vector”: jump to start of main program
    Interrupt “vector”: jump to start of ISR
Code from program:
Org 0x0 ;Reset Vector starts at 0x0000
bra Start ;main code execution
Org 0x0004 ;Interrupt Vector starts at
; address 0x0004
goto ISR

## Slide 14: Interrupt setup
Need to enable necessary interrupts
  GIE bit in INTCON register: global interrupt enable
  Timer 0 “rolls over” (goes from 255 to 0)
    Set TMR0IE bit in INTCON
  Switch is pressed (pin RA2 goes from high to low)
    Interrupt on negative edge change in port A, pin 2
    IOCIF flag in INTCON: general enable for interrupt on change
    Bit 2 in IOCAN register: negative edge interrupt for port A, pin 2
Flags set when interrupt occurs
  TMR0IF in INTCON for Timer 0 interrupt
  Bit 2 of IOCAF register for switch
    IOCAF  checking for interrupt on change in port A
  Software must clear flags, or interrupts repeatedly occur

## Slide 15: Rotate with interrupts (asm): Setup (1/3)
#define SWITCH PORTA, 2 ;pin where SW1 is connected
#define PULL_UPS ;if this is uncommented, JP5 can be pulled out
#define LED_RIGHT 0xFF ;keep track of LED direction
#define LED_LEFT 0x00
cblock 0x70 ;shared memory accessible from all banks
Direction
Delay1
endc
Org 0x0 ;Reset Vector starts at 0x0000
bra Start ;main code execution
Org 0x0004 ;Interrupt Vector starts at address 0x0004
goto ISR
Start:
banksel OSCCON ;bank1
movlw b'00111000' ;set cpu clock speed FO 500KHz
movwf OSCCON
bsf TRISA, RA2 ;switch as input
banksel ANSELA ;bank3
bcf ANSELA, RA2 ;digital
;can reference pins by position or name

## Slide 16: Rotate with interrupts (asm): Setup (2/3)
;Configure the LEDs
banksel TRISC ;bank1
clrf TRISC ;make all of PORTC an output
banksel LATC ;bank2
movlw b'00001000' ;start with DS4 lit
;Setup Timer0 as the delay
banksel OPTION_REG ;bank1
movlw b'00000111' ;1:256 prescaler for a delay of 524mS
movwf OPTION_REG
bsf INTCON, TMR0IE ;enable the rollover interrupt to occur
;Setup interrupt-on-change for the switch
bsf INTCON, IOCIE ;set global IOC enable flag
banksel IOCAN ;bank7
bsf IOCAN, IOCAN2 ;when SW1 is pressed, enter the ISR
bsf INTCON, GIE ;must set GIE to allow any interrupt

## Slide 17: Rotate with interrupts (asm): Setup (3/3)
#ifdef PULL_UPS ;set up pull up resistors
banksel WPUA ;bank4
bsf WPUA, 2 ;enable pull-up for switch
banksel OPTION_REG ;bank1
;enable (clear) the global weak pull-up bit
bcf OPTION_REG, NOT_WPUEN
#endif
movlw LED_RIGHT ; LEDs start moving
movwf Direction ; to right
;Clear the RAM
clrf Delay1

## Slide 18: Rotate with interrupts (asm): Main loop, debounce, rotate LEDs
MainLoop:
bra MainLoop ; Main program doesn’t have to wait for timer
Debounce: ; Delay for ~5 mS
movlw d'209' ;(1/(500KHz/4))*209*3 = 5.016mS
movwf Delay1
DebounceLoop:
decfsz Delay1, f
bra DebounceLoop
return
RotateRight:
lsrf LATC, f ;logical shift right
btfsc STATUS,C ;did the bit rotate into the carry?
bsf LATC,3 ;yes, put it into bit 3.
retfie
RotateLeft:
lslf LATC, f ;logical shift left
btfsc LATC, 4 ;did it rotate out of the LED display?
bsf LATC, 0 ;yes, put in bit 0
retfie

## Slide 19: Rotate with interrupts (asm): ISR (1/2)
ISR:
banksel IOCAF ;bank7
btfsc IOCAF, 2 ;check the interrupt-on-change flag
bra Service_SW1 ;switch was pressed
bra Service_TMR0 ;Timer0 overflowed
Service_SW1:
; Clear flag without changing other IOCAF bits
movlw 0xFF
xorwf IOCAF, w
andwf IOCAF, f ;clearing this will also clear INTCON, IOCIF bit
call Debounce ;delay for 5ms and check switch again
banksel PORTA ;bank0
btfsc SWITCH ;is it still held down?
retfie ;nope, exit the ISR back to the main code
movlw 0xFF
xorwf Direction, f ;toggle direction state and save it back
retfie ;return to main code

## Slide 20: Rotate with interrupts (asm): ISR (2/2)
Service_TMR0:
bcf INTCON, T0IF ; clear flag
banksel LATC
movlw LED_RIGHT ; check dir
subwf Direction, w
btfsc STATUS, Z
bra RotateRight
bra RotateLeft
end ;end code generation

## Slide 21: Rotate with interrupts (C): defines
#include <htc.h> //PIC hardware mapping
#define _XTAL_FREQ 500000 //Used by the XC8 delay_ms(x) macro
#define DOWN 0
#define UP 1
#define SWITCH PORTAbits.RA2
#define LED_RIGHT 1
#define LED_LEFT 0
#define PULL_UPS
//config bits that are part-specific for the PIC16F1829
__CONFIG(FOSC_INTOSC & WDTE_OFF & PWRTE_OFF & MCLRE_OFF & CP_OFF & CPD_OFF & BOREN_ON & CLKOUTEN_OFF & IESO_OFF & FCMEN_OFF);
__CONFIG(WRT_OFF & PLLEN_OFF & STVREN_OFF & LVP_OFF);

## Slide 22: Rotate with interrupts (C): main (1/2)
unsigned char _direction; //a global variable
void main(void) {
//general init
OSCCON = 0b00111000; //500KHz clock speed
TRISC = 0; //all LED pins are outputs
LATC = 0; //init LEDs in OFF state
LATCbits.LATC3 = 1; //DS4 is lit
_direction = LED_RIGHT; //LEDs rotating R to L
//setup switch (SW1)
TRISAbits.TRISA2 = 1; //switch as input
ANSELAbits.ANSA2 = 0; //digital switch
//by using internal resistors, you eliminate external pull-up/down resistor
#ifdef PULL_UPS
WPUA2 = 1; //enable weak pull-up for switch
nWPUEN = 0; //enable global weak pull-up bit
#endif

## Slide 23: Rotate with interrupts (C): main (2/2)
//setup TIMER0 as the delay
//1:256 prescaler for a delay of: (insruction-cycle * 256-counts)*prescaler = ((8uS * 256)*256) =~ 524mS
OPTION_REG = 0b00000111; //setup TIMER0
INTCONbits.TMR0IE = 1; //enable the TMR0 rollover interrupt
//setup interrupt on change for the switch
INTCONbits.IOCIE = 1; //enable interrupt on change global
IOCANbits.IOCAN2 = 1; //when SW1 is pressed, enter the ISR
GIE = 1; //enable global interupts
while (1) {
continue; //can spend rest of time doing something critical here
}
}

## Slide 24: Rotate with interrupts (C): ISR
void interrupt ISR(void) {
if (IOCAF) { //SW1 was just pressed
IOCAF = 0; //must clear the flag in software
__delay_ms(5); //debounce by waiting and seeing if still held down
if (SWITCH == DOWN) {
_direction ^= 1; //change directions
}
}
if (INTCONbits.T0IF) {
INTCONbits.T0IF = 0;
if (_direction == LED_RIGHT) {
LATC >> = 1; //rotate right
if (STATUSbits.C == 1) //when the last LED is lit, restart the pattern
LATCbits.LATC3 = 1;
} else{
LATC << = 1; //rotate left
if (LATCbits.LATC4 == 1) //when the last LED is lit, restart the pattern
LATCbits.LATC0 = 1;
}
}
}

## Slide 25: Final notes
Next time:
  Continue PIC programming: analog to digital conversion
Reminders:
  HW 8: Working with PICkits—groups of up to 4 (3 preferred)
    Due 12/9 by 2:30 PM
  HW 9 to be posted; also due 12/9 by 2:30 PM
    Individual problem set