## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Spring 2016
Lecture 24:
PIC instruction set (continued)
PIC assembly programming

## Slide 2: Lecture outline
Announcements/reminders
  HW 7 to be posted; due date TBD
  Exams returned Monday
Today’s lecture
  Finish PIC instruction set
  Common simple operations

## Slide 3: Miscellaneous
Notes:
clrwdt ; if watchdog timer is enabled, this instruction will reset
; it (before it resets the CPU)
sleep ; Stop clock; reduce power; wait for watchdog timer or
; external signal to begin program execution again
nop ; Do nothing; wait one clock cycle
clrwdt ; clear watchdog timer
sleep ; go into standby mode
reset ; software reset
nop ; no operation
STATUS bits:
clrwwdt, sleep:
NOT_TO, NOT_PD
nop: none

## Slide 4: Working with multiple registers
Can’t do simple data transfer or operation on two registers
Usually must involve working register
Examples (assume X, Y file registers):
  X = Y
    movf Y, W
    movwf X
  X = X + Y
    movf Y, W
    addwf X, F

## Slide 5: Conditional jumps
Basic ones are combination of bit tests, skips
Remember that condition you’re testing is opposite of jump condition
Examples:
  Jump to label if carry == 0 (similar to x86 JNC)
    btfss STATUS, C
    goto label
  Jump if result of comparison is equal (~x86 JE)
    btfsc STATUS, Z
    goto label

## Slide 6: Conditional jumps (cont.)
To evaluate other conditions, may want to use subtraction in place of compare
Comparing X & Y turns into:
  movf Y, W
  subwf X, W
Possible results (unsigned comparison only):
  X > Y  Z = 0, C = 1
  X == Y  Z = 1, C = 1
  X < Y  Z = 0, C = 0
More complex conditions
  X <= Y  Z == C
  X != Y  Z = 0
  X >= Y  C = 1

## Slide 7: Shift/rotate operations
May need to account for bit being shifted/rotated out
  Basic rotate doesn’t rotate through carry
  Can either pre-test or fix later
Multi-bit shift/rotate: loop where # iterations matches shift amount

## Slide 8: Shift/rotate operations (cont.)
Examples:
  Rotate X to the right by 1 without the carry
    bcf STATUS, C ; Clear carry bit
    rrf X, F ; Rotate X one bit to right
    btfsc STATUS, C ; Skip next instruction if C clear
    ; C = bit shifted out of MSB
    bsf X, 7 ; Handle case where C = 1
    ; MSB of X should be 1
  Rotate X through the carry to the left by 3
    movlw 3 ; Initialize working register to 3 (# iterations)
    movwf COUNT ; Initialize count register
    ; Assumes you’ve declared variable COUNT
    Loop: rlf X, F ; Rotate Xone bit to left
    decfsz COUNT, F ; Decrement counter & test for 0
    ; Skip goto if result is zero
    goto Loop ; Return to start to loop

## Slide 9: Examples
Translate these x86 operations to PIC code
Assume that there are registers defined for each x86 register (e.g. AL, AH, BL, BH, etc.)
  Note: there is no actual translation from x86 to PIC
OR AL, BL
SUB BL, AL
JNZ label
JB label (B = below = unsigned <)
ROL AL, 5

## Slide 10: Example solution
OR AL, BL
  movf BL, W ; W = BL
  iorwf AL, F ; AL = AL OR W = AL OR BL
SUB BL, AL
  movf AL, W ; W = AL
  subwf BL, F ; BL = BL – W = BL – AL
JNZ label
  btfss STATUS, Z ; Skip goto if Z == 1 (if
  goto label ; previous result == 0)

## Slide 11: Example solution (continued)
JB label
  btfsc STATUS, Z ; If Z == 0, check C
  goto End ; Otherwise, no jump
  btfss STATUS, C ; If C == 1, no jump
  goto label ; Jump to label
  End: ; End of jump

## Slide 12: Example solution (continued)
ROL AL, 5
  movlw 5 ; W = 5
  movwf COUNT ; COUNT = W = 5
  L: bcf STATUS, C ; C = 0
  btfsc AL, 7 ; Skip if MSB == 0
  bsf STATUS, C ; C = 1 if MSB == 1
  ; C will hold copy of
  ; MSB (bit rotated into
  ; LSB)
  rlf AL, F ; Rotate left by 1
  decfsz COUNT ; If COUNT == 0, don’t
  ; restart loop
  goto L

## Slide 13: Final notes
Next time:
  More PIC programming + return exams
Reminders:
  HW 7 to be posted; due date TBD
  Exams returned Monday