## Slide 1: 16.216 ECE Application Programming
Instructors:
Dr. Michael Geiger & Dr. Peilong Li
Spring 2017
Lecture 36
Bitwise operators (continued)

## Slide 2: Lecture outline
Announcements/reminders
  Exam 3 Q & A session next week (W/Th)?
  Program 9 due 4/28
    No late penalties—only extra credit
    +15% for submitting assignment “on time” (by 4/28)
    +10% for submitting assignment 4/29-5/1
    +5% for submitting assignment 5/2-5/4
  All outstanding program regrades due 4/28
    Remember, e-mail the appropriate TA and CC your instructor when you resubmit—do not just e-mail Dr. Geiger
  Exam 2 resubmissions due 4/28
    Receive credit for Question 2b
Review
  Bitwise operators
Today’s lecture
  Applications of bitwise operators

## Slide 3: Review: bit manipulation
Bitwise operators: | & ^ ~
  Used for desired logical operations
  Used to set/clear bits
Bit shifts: << >>
  Used to shift bits into position
  Used for multiplication/division by powers of 2

## Slide 4: Example: Common bitwise operations
Given an unsigned int, n, and a number, b, how would you:
  Clear all bits of n?
  Clear the lower 16 bits of n (mask out lower bits)?
  Flip all bits of n?
  Flip bit b of n?
  Set bit b of n (i.e., make sure bit b is 1)?
  Clear bit b of n (i.e., make sure bit b is 0)?
Note: 0 ≤ b ≤ 31; least significant (rightmost) bit is bit 0

## Slide 5: Example solution
Given an unsigned int, n, and a number, b, how would you:
  Clear all bits of n?
    n = 0;
  Clear the lower 16 bits of n (mask out lower bits)?
    X & 0 = 0, regardless of whether X = 0 or X = 1
      Should AND lower 16 bits with 0
    n = n & 0xFFFF0000;
  Flip all bits of n?
    n = ~n;

## Slide 6: Example solution (cont.)
Given an unsigned int, n, and a number, b, how would you:
  Flip bit b of n?
    X ^ 1 = ~X, regardless of whether X = 0 or X = 1
    Need 1 in bit position b  (1 << b)
    n = n ^ (1 << b);
  Set bit b of n (i.e., make sure bit b is 1)?
    X | 1 = 1, regardless of whether X = 0 or X = 1
    n = n | (1 << b);
  Clear bit b of n (i.e., make sure bit b is 0)?
    As shown before, X & 0 = 0
    To get 0 in specific bit position, shift 1 to that position and then invert bit mask: ~(1 << b)
    n = n & ~(1 << b);

## Slide 7: Common bitwise operations
General operation | Logical operation | Bit mask values in positions that change | Bit mask values in positions staying same | Example: modify bits 8-23 (middle 16 bits)
Set bit(s) Bits changed to 1 | OR | 1 | 0 | n = n ¦ 0x00FFFF00
Clear bit(s) Bits changed to 0 | AND | 0 | 1 | n = n & 0xFF0000FF
Flip bit(s) All 0  1; All 1  0 | XOR | 1 | 0 | n = n ^ 0x00FFFF00

## Slide 8: Extracting bits
Very common to extract bits from larger value
  One example: instruction decoding
    Instruction: basic operation executed by processor
    Decoding: figure out what each bit group “means”
      First bits typically operation; others choose data to be used
  Examples: 0xABCD1234 =
  1010 1011 1100 1101 0001 0010 0011 01002
    Lowest 16 bits = 0x1234
    Upper 16 bits = 0xABCD
    Bits 24-31 = 0xAB
    Bits 1-6  look at lowest 8 bits (bits 0-7)
      001101002  bits 1-6 = 011010 = 0x1A

## Slide 9: Extracting bits (cont.)
Isolate bits you want
  AND with bit mask to clear unwanted bits
    Positions you want to keep = 1
    Positions you want to clear = 0
  Examples:
    To get lowest 16 bits  mask = 0x0000FFFF
    To get upper 16 bits  mask = 0xFFFF0000
    To get bits 24-31  mask = 0xFF000000
    To get bits 1-6  mask = 0...0 0111 11102 = 0x0000007E

## Slide 10: Extracting bits (cont.)
Shift bits to right
  Shift amount = original position of lowest bit
  Examples:
    Lowest 16 bits  bits 0-15  no shift
    Upper 16 bits  bits 16-31  shift right by 16
    Bits 24-31  shift right by 24
    Bits 1-6  shift right by 1
Order doesn’t really matter
  Could shift first and then AND to mask out upper bits
Can combine steps in single operation
  Examples:
    Upper 16 bits of x = (x & 0xFFFF0000) >> 16
    Bits 1-6 of x = (x & 0x0000007E) >> 1

## Slide 11: Hexadecimal output
To print a number in hex, use %x or %X
  %x prints characters a-f in lowercase
  %X prints characters A-F in uppercase
To show leading 0x, use the # flag
To show leading 0s, use precision with total # digits
  Field width + 0 flag also works unless value = 0
Examples (assume var1 = 0x1A2B)
  printf(“%x”, var1)  1a2b
  printf(“%X”, var1)  1A2B
  printf(“%#x”, var1)  0x1a2b
  printf(“%.6x”, var1)  001a2b
  printf(“%#.6x”, var1)  0x001a2b

## Slide 12: Final notes
Next time
  Exam 3 Preview
Reminders:
  Exam 3 Q & A session next week (W/Th)?
  Program 9 due 4/28
    No late penalties—only extra credit
    +15% for submitting assignment “on time” (by 4/28)
    +10% for submitting assignment 4/29-5/1
    +5% for submitting assignment 5/2-5/4
  All outstanding program regrades due 4/28
    Remember, e-mail the appropriate TA and CC your instructor when you resubmit—do not just e-mail Dr. Geiger
  Exam 2 resubmissions due 4/28
    Receive credit for Question 2b