## Slide 1: 16.317 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2015
Lecture 23:
PIC instruction set (continued)
PIC assembly programming

## Slide 2: Lecture outline
Announcements/reminders
  HW 4 due 2:00 PM, 10/30
  Wednesday, November 4: Exam 2
    Will be allowed one double-sided 8.5” x 11” note sheet, calculator
    Instruction list to be provided
    Covers material through Monday (W, F lectures not on exam)
Review
  Control flow instructions
  Conditional execution
Today’s lecture
  Finish PIC instruction set
  Common simple operations

## Slide 3: Review: Control flow instructions
Unconditional jumps
  goto
  bra/brw
Call/return instructions
  call/callw
  return/retlw/retfie

## Slide 4: Review: Conditional Execution
Examples:
btfsc TEMP1, 0 ; Skip the next instruction if bit 0 of TEMP1 equals 0
btfss STATUS, C ; Skip the next instruction if C==1
decfsz TEMP1, F ; Decrement TEMP1, skip if TEMP1==0
incfsz TEMP1, W ; W <- TEMP1+1 , skip if W==0 (TEMP1==0xFF)
; Leave TEMP1 unchanged
btfsc f, b ;Test bit b of register f, where b=0 to 7, skip if clear
btfss f, b ;Test bit b of register f, where b=0 to 7, skip if set
decfsz f, F(W) ;decrement f, putting result in F or W, skip if zero
incfsz f, F(W) ;increment f, putting result in F or W, skip if zero
STATUS bits:
none
Conditional execution in PIC: skip next instruction if condition true
Two general forms
  Test bit and skip if bit clear/set
  Increment/decrement register and skip if result is 0

## Slide 5: Miscellaneous
Notes:
clrwdt ; if watchdog timer is enabled, this instruction will reset
; it (before it resets the CPU)
sleep ; Stop clock; reduce power; wait for watchdog timer or
; external signal to begin program execution again
nop ; Do nothing; wait one clock cycle
clrwdt ; clear watchdog timer
sleep ; go into standby mode
reset ; software reset
nop ; no operation
STATUS bits:
clrwwdt, sleep:
NOT_TO, NOT_PD
nop: none

## Slide 6: Working with multiple registers
Can’t do simple data transfer or operation on two registers
Usually must involve working register
Examples: x86  PIC (assume PIC registers defined with same names as x86 registers)
  MOV AL, BL
    movf BL, W
    movwf AL
  ADD AL, BL
    movf BL, W
    addwf AL, F

## Slide 7: Conditional jumps
Basic ones are combination of bit tests, skips
Remember that condition you’re testing is opposite of jump condition
Examples: x86  PIC
  JNC label
    btfss STATUS, C
    goto label
  JE label
    btfsc STATUS, Z
    goto label

## Slide 8: Conditional jumps (cont.)
To evaluate other conditions, may want to use subtraction in place of compare
CMP X, Y turns into:
  movf Y, W
  subwf X, W
Possible results (unsigned comparison only):
  X > Y  Z = 0, C = 1
  X == Y  Z = 1, C = 1
  X < Y  Z = 0, C = 0
More complex conditions
  X <= Y  Z == C
  X != Y  Z = 0
  X >= Y  C = 1

## Slide 9: Shift/rotate operations
May need to account for bit being shifted/rotated out
  Basic rotate doesn’t rotate through carry
  Can either pre-test or fix later
Multi-bit shift/rotate: loop where # iterations matches shift amount

## Slide 10: Shift/rotate operations (cont.)
Examples: x86  PIC
  ROR AL, 1
    bcf STATUS, C ; Clear carry bit
    rrf AL, F ; Rotate AL one bit to right
    btfsc STATUS, C ; Skip next instruction if C clear
    ; C = bit shifted out of MSB
    bsf AL, 7 ; Handle case where C = 1
    ; MSB of AL should be 1
  RCL AL, 3
    movlw 3 ; Initialize working register to 3 (# iterations)
    movwf COUNT ; Initialize count register
    ; Assumes you’ve declared variable COUNT
    Loop: rlf AL, F ; Rotate AL one bit to left
    decfsz COUNT, F ; Decrement counter & test for 0
    ; Skip goto if result is zero
    goto Loop ; Return to start to loop

## Slide 11: Examples
Translate these x86 operations to PIC code
Assume that there are registers defined for each x86 register (e.g. AL, AH, BL, BH, etc.)
OR AL, BL
SUB BL, AL
JNZ label
JB label (B = below = unsigned <)
ROL AL, 5

## Slide 12: Example solution
OR AL, BL
  movf BL, W ; W = BL
  iorwf AL, F ; AL = AL OR W = AL OR BL
SUB BL, AL
  movf AL, W ; W = AL
  subwf BL, F ; BL = BL – W = BL – AL
JNZ label
  btfss STATUS, Z ; Skip goto if Z == 1 (if
  goto label ; previous result == 0)

## Slide 13: Example solution (continued)
JB label
  btfsc STATUS, Z ; If Z == 0, check C
  goto End ; Otherwise, no jump
  btfss STATUS, C ; If C == 1, no jump
  goto label ; Jump to label
  End: ; End of jump

## Slide 14: Example solution (continued)
ROL AL, 5
  movlw 5 ; W = 5
  movwf COUNT ; COUNT = W = 5
  L: bcf STATUS, C ; C = 0
  btfsc AL, 7 ; Skip if MSB == 0
  bsf STATUS, C ; C = 1 if MSB == 1
  ; C will hold copy of
  ; MSB (bit rotated into
  ; LSB)
  rlf AL, F ; Rotate left by 1
  decfsz COUNT ; If COUNT == 0, don’t
  ; restart loop
  goto L

## Slide 15: Final notes
Next time:
  More PIC programming
Reminders:
  HW 4 due 2:00 PM, 10/30
  Wednesday, November 4: Exam 2
    Will be allowed one double-sided 8.5” x 11” note sheet, calculator
    Instruction list to be provided
    Covers material through Monday (W, F lectures not on exam)