## Slide 1: 16.317 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2015
Lecture 3:
Data (continued): storage media, alignment, and endianness

## Slide 2: Lecture outline
Announcements/reminders
  Sign up for the course discussion group on Piazza
  HW 1 to be posted this week
Review
  Data types
    How are the bits interpreted? (int, FP, signed/unsigned)
    What size are they? (byte, word, etc.)
Today’s lecture
  Storage media
  Alignment
  Endianness

## Slide 3: Data storage
What characteristics do we want storage media to have?
Two primary answers
  Speed
  Capacity
  Very difficult to get both in single storage unit
Processors use two different types of storage
  Registers
  Memory

## Slide 4: Registers
Small, fast set of storage locations close to processor core (execution engine)
Primarily used for computation, short-term storage
  Speed  ideal for individual operations
  Lack of capacity  will frequently overwrite
Reference registers by name
  Example: ADD EAX, EBX  EAX = EAX + EBX
  EAX, EBX are registers in x86 architecture

## Slide 5: Memory
Provides enough capacity for all code, data (possibly I/O as well)
Typically organized as hierarchy
Used primarily for long-term storage
  Lacks speed of registers
  Provides capacity to ensure data not overwritten
Reference memory by address
  Example: MOV EAX, DS:[100H]
   EAX = memory at address DS:[100H]

## Slide 6: Memory (continued)
Accessing single byte is easy
Considerations with multi-byte data
  Are the data aligned?
    Easier/faster to access aligned data
  How are the data organized in memory (“endianness”)?
    Given 32-bit number: DEADBEEFH or 0xDEADBEEF
    Which byte—MSB (0xDE) or LSB (0xEF) gets stored in memory first?

## Slide 7: Aligned Words, Double words
Aligned data: address is divisible by # of bytes
  2 bytes  address must be even
  4 bytes  address must be multiple of 4
x86 architecture doesn’t require aligned data access
  Performance impact for accessing unaligned data in memory (32-bit data bus)
Byte address |  |  |  |  | 
0 |  |  |  |  | 
4 |  |  |  |  | 
8 |  |  |  |  | 
12 |  |  |  |  | 
16 |  |  |  |  | 
20 |  |  |  |  | 
Aligned word
Aligned double word
Unaligned
word
Unaligned
double
word

## Slide 8: Byte order (“endianness”)
In a multi-byte operand, how are the bytes ordered in memory?
Assume the double word value 1,000,000 (0x000F4240) is stored at address 80
  In a little-endian ISA (like x86), the least significant byte (the “little” end) is at address 80
  In a big-endian ISA (like MIPS), it’s the other way around
 |  | 00 | 0F | 42 | 40 |  | 
… | 79 | 80 | 81 | 82 | 83 | 84 | …
 |  | 40 | 42 | 0F | 00 |  | 
… | 79 | 80 | 81 | 82 | 83 | 84 | …

## Slide 9: Examples
Given the following memory contents:
  Starting address of each line shown on left
  Leftmost byte has lowest address
    First line: addresses 0x200C, 0x200D, 0x200E, 0x200F
What is the value of:
  The word starting at address 0x200D?
  The double word starting at address 0x2012?
Are these data aligned?
 | Lo |  |  | Hi
0x200C | 40 | 96 | 2C | 00
0x2010 | 55 | 12 | CD | AB
0x2014 | 01 | 23 | 88 | 99

## Slide 10: Solution
Word at 0x200D = 0x2C96
  Address is not divisible by 2  unaligned
Double word at 0x2012 = 0x2301ABCD
  Address is not divisible by 4  unaligned
    Remember, hexadecimal is base 16—0x12 = 1810
 | Lo |  |  | Hi
0x200C | 40 | 96 | 2C | 00
0x2010 | 55 | 12 | CD | AB
0x2014 | 01 | 23 | 88 | 99

## Slide 11: Final notes
Next time:
  Assembly programming basics
Reminders:
  Sign up for the discussion group on Piazza
  HW 1 to be posted this week; due date TBD