## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2016
Lecture 7:
Arithmetic instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 2 due 2:00 PM today
  HW 3 to be posted; due 2:00 PM 9/28
Review
  Data transfer instructions (XCHG, LEA)
Today’s lecture
  Arithmetic instructions

## Slide 3: Review: XCHG, LEA
XCHG: swap contents of source, dest
  For example, if AX = 0x1234 and BX = 0x5678:
  XCHG AX, BX  AX = 0x5678, BX = 0x1234
LEA: load effective address
  Store result of effective address computation in register
  Instruction doesn’t actually access memory
  For example, given AX = 0x3170:
  LEA CX, [AX+0x0220]  CX = 0x3390

## Slide 4: Flags
All arithmetic instructions set flags
  CF = carry flag (carry output from MSB of add/sub)
  OF = overflow flag
  ZF = zero flag (result is zero)
  SF = sign flag (1 if negative, 0 if positive)
  PF = parity flag (even parity in LSB)
  AF = auxiliary carry (carry between nibbles)
Stored in FLAGS register
Referenced in conditional instructions

## Slide 5: Addition instructions
ADD D, S
  Operation: (D) = (D) + (S)
ADC D, S
  Operation: (D) = (D) + (S) + (CF)
INC D
  Operation: (D) = (D) + 1

## Slide 6: Subtraction instructions
SUB D, S
  Operation: (D) = (D) – (S)
SBB D, S
  Operation: (D) = (D) – (S) – (CF)
DEC D
  Operation: (D) = (D) – 1
NEG D
  Operation: (D) = -(D)
  Two’s complement negation

## Slide 7: Addition/subtraction examples
Given the following initial state:
  AX = 0x1234
  BL = 0xAB
  Memory location SUM = 0x00CD
Show the results of each step of the following instruction sequence:
  ADD AX, [SUM]
  ADC BL, 0x05
  NEG BL
  SUB AX, 0x12
  INC WORD PTR [SUM]

## Slide 8: Example solution
ADD AX, [SUM]
  AX = (SUM) + AX
  0x00CD + 0x1234 = 0x1301
  AX = 0x1301, CF = 0
ADC BL, 05h
  BL = BL + 0x05 + CF
  0xAB + 0x05 + 0 = 0xB0
  BL = 0xB0, CF = 0
NEG BL
  BL = –BL
  –0xB0 = –(1011 0000)2 = 0101 00002 = 0x50

## Slide 9: Example solution (cont.)
SUB AX, 0x12
  AX = AX – 0x0012
  0x1301 – 0x0012 = 0x12EF
  AX = 0x12EF, CF = 0
INC WORD PTR [SUM]
  (SUM) = (SUM) + 1
  0x00CD + 1 = 0x00CE
  (SUM) = 0x00CE, CF = 0

## Slide 10: Final notes
Next time:
  Multiplication and division
  Logical and shift instructions
Reminders:
  HW 2 due 2:00 PM today
  HW 3 to be posted; due 2:00 PM 9/28