## Slide 1: 16.317 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2015
Lecture 25:
PIC assembly programming (continued)

## Slide 2: Lecture outline
Announcements/reminders
  HW 5 to be posted; due date TBD
Today’s lecture
  Sample programming sequences

## Slide 3: A Delay Subroutine
; ***********************************************************************************
; TenMs subroutine and its call inserts a delay of exactly ten milliseconds
; into the execution of code.
; It assumes a 4 MHz crystal clock. One instruction cycle = 4 * Tosc.
; TenMsH equ 13 ; Initial value of TenMs Subroutine's counter
; TenMsL equ 250
; COUNTH and COUNTL are two variables
TenMs
nop ; one cycle
movlw TenMsH ; Initialize COUNT
movwf COUNTH
movlw TenMsL
movwf COUNTL
Ten_1
decfsz COUNTL,F ; Inner loop
goto Ten_1
decfsz COUNTH,F ; Outer loop
goto Ten_1
return

## Slide 4: Blinking LED example
Assume three LEDs (Green, Yellow, Red) are attached to Port D bit 0, 1 and 2. Write a program for the PIC16F874 that toggles the three LEDs every half second in sequence: green, yellow, red, green, ….
For this example, assume that the system clock is 4MHz.

## Slide 5: Top Level Flowchart
Initialize: Initialize port D, initialize the counter for 500ms.
Blink: Toggle the LED in sequence, green, yellow, red, green, …. Which LED to be toggled is determined by the previous state.
Wait for 500ms: Keep the LED on for 500ms and then toggle the next one.

## Slide 6: Strategy to “Blink”
The LEDs are toggled in sequence - green, yellow, red, green, yellow, red…
Let’s look at the lower three bits of PORTD
  001=green, 010=yellow, 100=red
The next LED to be toggled is determined by the current LED.
001->010->100->001->…

## Slide 7: “Blink” Subroutine
Blink
btfsc PORTD, 0 ; is it Green?
goto toggle1 ; yes, goto toggle1
btfsc PORTD, 1 ; else is it Yellow?
goto toggle2 ; yes, goto toggle2
;toggle0
bcf PORTD, 2 ; otherwise, must be red, change to green
bsf PORTD, 0 ; 100->001
return
toggle1
bcf PORTD, 0 ; change from green to yellow
bsf PORTD, 1 ; 001->010
return
toggle2
bcf PORTD, 1 ; change from yellow to red
bsf PORTD, 2 ; 010->100
return

## Slide 8: Another way to code “Blink” ---- Table Use
BlinkTable
movf PORTD, W ; Copy present state of LEDs into W
andlw B'00000111' ; and keep only LED bits
addwf PCL,F ; Change PC with PCLATH and offset in W
retlw B'00000001' ; (000 -> 001) reinitialize to green
retlw B'00000011' ; (001 -> 010) green to yellow
retlw B'00000110' ; (010 -> 100) yellow to red
retlw B'00000010' ; (011 -> 001) reinitialize to green
retlw B'00000101' ; (100 -> 001) red to green
retlw B'00000100' ; (101 -> 001) reinitialize to green
retlw B'00000111' ; (110 -> 001) reinitialize to green
retlw B'00000110' ; (111 -> 001) reinitialize to green
In calling program
call BlinkTable ; get bits to change into W
xorwf PORTD, F ; toggle them into PORTD

## Slide 9: Application: Driving stepper motor
Magnet attached to shaft
Current through coil  magnetic field
  Reverse current  reverse field
Pair of coils used to attract magnet to one of 4 different directions
Unipolar stepper motor: center taps on coil make current reversal easy
  Microcontroller can activate drive transistors
Magnet rotor
coil
Notes: Major differences between uni-polar and bi-polar.
Uni-polar
has logically two windings per phase, so a magnetic pole can be reversed without switching the direction of current,
A microcontroller or stepper motor controller can be used to activate the drive transistors in the right order,
Less torque
bi-polar
has logically a single winding per phase, so current in a winding needs to be reversed in order to reverse a magnetic pole,
driving circuit must be more complicated, typically with an H-bridge arrangement
More torque

## Slide 10: How Bi-polar Stepper Motor Works
Bipolar stepper motor
  More torque than unipolar motor
  Similar principle, but no center taps
    Need glue circuitry (use H-bridge)

## Slide 11: Sequences (1 = phase activated)
Table of Stepping Sequences
Sequence | Polarity | Name | Description
0001 0010 0100 1000 | ---+ --+- -+-- +--- | Wave Drive, One-Phase | Consumes the least power. Only one phase is energized at a time. Assures positional accuracy regardless of any winding imbalance in the motor.
0011 0110 1100 1001 | --++ -++- ++-- +--+ | Hi-Torque, Two-Phase | Hi Torque - This sequence energizes two adjacent phases, which offers an improved torque-speed product and greater holding torque.
0001 0011 0010 0110 0100 1100 1000 1001 | ---+ --++ --+- -++- -+-- ++-- +--- +--+ | Half-Step | Half Step - Effectively doubles the stepping resolution of the motor, but the torque is not uniform for each step. (Since we are effectively switching between Wave Drive and Hi-Torque with each step, torque alternates each step.) Note that this sequence is 8 steps.

## Slide 12: The Schematic
Notes: Because of power requirements, induction of the windings, and temperature management, motors cannot be directly powered by most digital controllers. Some "glue circuitry," such as a motor controller (H-bridge) is necessary between digital controller and motor. The above image shows the basic circuit of a motor controller which can also sense motor current. (One wire of the motor is shown; a stepper motor would require such a circuit for four wires, and a normal DC motor for two. This circuitry is typically all included in an integrated H-bridge chip.

## Slide 13: Our energization pattern
Step | Up-down Coil | East-West Coil
1 | South | Off
2 | South | South
3 | Off | South
4 | North | South
5 | North | Off
6 | North | North
7 | Off | North
8 | South | North

## Slide 14: Our control sequence
RC5 | RC4 | RC3 | RC2
0 | 1 | 1 | 1
0 | 1 | 0 | 1
0 | 0 | 0 | 1
1 | 0 | 0 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
0 | 1 | 1 | 0

## Slide 15: Sequence 0111
0
1
1
1
OFF

## Slide 16: Sequence 0101
0
1
0
1

## Slide 17: The code (comments, directives)
title "asmStepper - PIC16F684 Bipolar Stepper Motor Control"
;
; This Program Outputs a new Bipolar Stepper Motor Sequence
; once every 250 ms.
;
; Hardware Notes:
; PIC16F684 running at 4 MHz Using the Internal Clock
; Internal Reset is Used
; RC5:RC2 - L293D Stepper Motor Control
;;
; Myke Predko
; 05.01.14
;
LIST R=DEC ;yluo note: list directive to specify assembler options
INCLUDE "p16f684.inc"
Notes: List directive is used to specify different assembly and listing commands to the assembler program.
R=DEC means the default number base in 10.
_CONFIG directive is used to specify the configuration word bits. Each parameter is ANDed together to specify which bits are reset and set.

## Slide 18: The Code (configuration code and data variables)
__CONFIG _FCMEN_OFF & _IESO_OFF & _BOD_OFF & _CPD_OFF & _CP_OFF & _MCLRE_OFF & _PWRTE_ON & _WDT_OFF & _INTOSCIO
; Variables
CBLOCK 0x20
Dlay, i
ENDC
PAGE
; Mainline
org 0
nop ; For ICD Debug

## Slide 19: The code (initialization)
movlw 1 << 2 ; Start with Bit 2 Active
movwf PORTC
movlw 7 ; Turn off Comparators
movwf CMCON0
bsf STATUS, RP0 ; Execute out of Bank 1
clrf ANSEL ^ 0x080 ; All Bits are Digital
movlw b'000011' ; RC5:RC2 are Outputs
movwf TRISC ^ 0x080
bcf STATUS, RP0 ; Return Execution to Bank 0
clrf i

## Slide 20: The code (main loop)
Loop: ; Return Here for Next Value
movlw HIGH ((250000 / 5) + 256)
movwf Dlay
movlw LOW ((250000 / 5) + 256)
addlw -1 ; 250 ms Delay
btfsc STATUS, Z
decfsz Dlay, f
goto $ - 3
movf i, w
call SwitchRead
movwf PORTC
incf i, f ; i = (i + 1) % 8;
bcf i, 3
goto Loop
SwitchRead:
addwf PCL, f ; Staying in First 256 Instructions
dt b'011100', b'010100', b'000100', b'100100'
dt b'100000', b'101000', b'111000', b'011000'
end

## Slide 21: Final notes
Next time:
  Return exams
Reminders:
  HW 5 to be posted, due date TBD