## Slide 1: 16.317 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2015
Lecture 6:
Data transfer instructions (cont.)
Arithmetic instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 1 due 2:00 PM, 9/18
Review
  Data transfer instructions
Today’s lecture
  Assembly basics
  Data transfer instructions

## Slide 3: Review: data & data transfer instructions
x86 data accesses
  Registers: access as 8-bit (e.g. AL, AH), 16-bit (AX), 32-bit (EAX)
  Memory
    Data size usually matches register
    If not, explicitly specify (BYTE PTR, WORD PTR, DWORD PTR)
MOV: basic data transfer
  Can use registers, memory, immediates
  If segment reg. is destination, source must be register

## Slide 4: Review: MOVSX/MOVZX
Move and extend data (fill upper bits with 0/1)
  ZX  zero extend
  SX  sign extend  copy MSB of source
Format: MOVZX D, S
MOVSX D, S
Operation: lower bits of D = S
upper bits of D = 0 (MOVZX) or
upper bits of D = MSB of S (MOVSX)
Restrictions
  Only register/memory operands (no immediates)
  Source must contain fewer bits than destination
  If memory operand used, size must be specified

## Slide 5: MOVSX/MOVZX examples
Assume: AX = 0100H, DX = 8100H,
(100H) = 00H, (101H) = FFH
What are the results of the following instructions?
MOVSX EBX, AX
MOVSX EBX, DX
MOVZX EBX, DX
MOVSX EBX, BYTE PTR [100H]
MOVSX EBX, WORD PTR [100H]

## Slide 6: MOVSX/MOVZX examples (soln)
Assume: AX = 0100H, DX = 8100H, (100H) = 00H, (101H) = FFH
What are the results of the following instructions?
MOVSX EBX, AX
  EBX = AX sign-extended = 00000100H (orig. value underlined)
MOVSX EBX, DX
  EBX = DX sign-extended = FFFF8100H
MOVZX EBX, DX
  EBX = DX zero-extended = 00008100H
MOVSX EBX, BYTE PTR [100H]
  EBX = byte at 100h sign-extended = 00000000H
MOVSX EBX, WORD PTR [100H]
  EBX = word at 100h sign-extended = FFFFFF00H

## Slide 7: XCHG
Swap contents of source and destination
Format: XCHG D, S
Operation: (D) = (S)
(S) = (D)
Restrictions:
  Memory operand can only be used as destination

## Slide 8: LEA
Perform effective address computation and store result in register
Format: LEA D, EA
Operation: D = EA
Example: LEA SI, [10H + DI]

## Slide 9: Example
 | Lo |  |  | Hi
0x528000 | 50 | 88 | 31 | A3
0x528004 | B2 | FF | 0F | 7D
0x528008 | 07 | D0 | BE | 22
0x52800C | 11 | 96 | 00 | 14
Given the initial memory contents at left, show the results of the following instruction sequence:
MOV EAX, 528000h
MOV EBX, [EAX+2]
XCHG BL, BH
LEA EDX, [EAX+8]
MOV ECX, [EDX-3]

## Slide 10: Solution
MOV EAX, 528000h
EAX = 528000h
MOV EBX, [EAX+2]
EBX = DWORD at 528002h = FFB2A331h
XCHG BL, BH
Swap BL and BH  EBX = FFB231A3h
LEA EDX, [EAX+8]
EDX = EAX+8 = 528008h
MOV ECX, [EDX-3]
ECX = DWORD at 528005h = 077D0FFFh

## Slide 11: Flags
All arithmetic instructions set flags
  CF = carry flag (carry output from MSB of add/sub)
  OF = overflow flag
  ZF = zero flag (result is zero)
  SF = sign flag (1 if negative, 0 if positive)
  PF = parity flag (even parity in LSB)
  AF = auxiliary carry (carry between nibbles)
Stored in FLAGS register
Referenced in conditional instructions

## Slide 12: Addition instructions
ADD D, S
  Operation: (D) = (D) + (S)
ADC D, S
  Operation: (D) = (D) + (S) + (CF)
INC D
  Operation: (D) = (D) + 1

## Slide 13: Subtraction instructions
SUB D, S
  Operation: (D) = (D) – (S)
SBB D, S
  Operation: (D) = (D) – (S) – (CF)
DEC D
  Operation: (D) = (D) – 1
NEG D
  Operation: (D) = -(D)
  Two’s complement negation

## Slide 14: Addition/subtraction examples
Given the following initial state:
  AX = 1234H
  BL = ABH
  Memory location SUM = 00CDH
Show the results of each step of the following instruction sequence:
  ADD AX, [SUM]
  ADC BL, 05H
  NEG BL
  SUB AX, 12H
  INC WORD PTR [SUM]

## Slide 15: Example solution
ADD AX, [SUM]
  (AX) = (DS:SUM) + (AX)
  00CDH + 1234H = 1301H
  (AX) = 1301H, (CF) = 0
ADC BL,05H
  (BL) = (BL) + IMM8 +(CF)
  ABH + 05H + 0 = B0H
  (BL) = B0H, (CF) = 0
NEG BL
  (BL) = –(BL)
  –B0H = –(1011 0000)2 = 0101 00002 = 50H

## Slide 16: Example solution (cont.)
SUB AX, 12H
  (AX) = (AX) – 0012H
  1301H – 0012H = 12EFH
  (AX) = 12EFH, (CF) = 0
INC WORD PTR [SUM]
  (DS:SUM) = (DS:SUM) + 1
  00CDH + 1 = 00CEH
  (SUM) = 00CEH, (CF) = 0

## Slide 17: Final notes
Next time:
  Multiplication and division
  Logical and shift instructions
Reminders:
  HW 1 due 2:00 PM, 9/18