## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Summer 2016
Lecture 3:
Arithmetic instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 1 due 1:00 PM today
  HW 2 to be posted; due 1:00 PM, 5/23
  Looking ahead: Exam 1 on Thursday, 5/26
    Will be allowed one double-sided 8.5” x 11” note sheet, calculator
    No other electronic devices allowed
    Instruction list will be provided (see website)
Review
  x86 data
  Data transfer instructions
Today’s lecture
  Arithmetic instructions

## Slide 3: Review: data & data transfer instructions
x86 data
  Registers: access as 8-bit (e.g. AL, AH), 16-bit (AX), 32-bit (EAX)
  Memory
    Data size usually matches register
    If not, explicitly specify (BYTE PTR, WORD PTR, DWORD PTR)
MOV: basic data transfer
  Can use registers, memory, immediates
MOVSX/MOVZX
  Sign-extend or zero-extend register/memory value

## Slide 4: Review: XCHG, LEA
XCHG: swap contents of source, dest
  For example, given AX = 1234h and BX = 5678h:
  XCHG AX, BX  AX = 5678h, BX = 1234h
LEA: load effective address
  Store result of effective address computation in register
  Instruction doesn’t actually access memory
  For example, given AX = 3170h:
  LEA CX, [AX+0220h]  CX = 3390h

## Slide 5: Flags
All arithmetic instructions set flags
  CF = carry flag (carry output from MSB of add/sub)
  OF = overflow flag
  ZF = zero flag (result is zero)
  SF = sign flag (1 if negative, 0 if positive)
  PF = parity flag (even parity in LSB)
  AF = auxiliary carry (carry between nibbles)
Stored in FLAGS register
Referenced in conditional instructions

## Slide 6: Addition instructions
ADD D, S
  Operation: (D) = (D) + (S)
ADC D, S
  Operation: (D) = (D) + (S) + (CF)
INC D
  Operation: (D) = (D) + 1

## Slide 7: Subtraction instructions
SUB D, S
  Operation: (D) = (D) – (S)
SBB D, S
  Operation: (D) = (D) – (S) – (CF)
DEC D
  Operation: (D) = (D) – 1
NEG D
  Operation: (D) = -(D)
  Two’s complement negation

## Slide 8: Addition/subtraction examples
Given the following initial state:
  AX = 1234h
  BL = ABh
  Memory location SUM = 00CDh
Show the results of each step of the following instruction sequence:
  ADD AX, [SUM]
  ADC BL, 05h
  NEG BL
  SUB AX, 12h
  INC WORD PTR [SUM]

## Slide 9: Example solution
ADD AX, [SUM]
  (AX) = (SUM) + (AX)
  00CDh + 1234h = 1301h
  (AX) = 1301h, (CF) = 0
ADC BL, 05h
  (BL) = (BL) + 05h +(CF)
  ABh + 05h + 0 = B0h
  (BL) = B0h, (CF) = 0
NEG BL
  (BL) = –(BL)
  –B0h = –(1011 0000)2 = 0101 00002 = 50h

## Slide 10: Example solution (cont.)
SUB AX, 12h
  (AX) = (AX) – 0012h
  1301h – 0012h = 12EFh
  (AX) = 12EFh, (CF) = 0
INC WORD PTR [SUM]
  (SUM) = (SUM) + 1
  00CDh + 1 = 00CEh
  (SUM) = 00CEh, (CF) = 0

## Slide 11: Multiplication/division
Both signed and unsigned integer versions
Register A is always one of the sources
Destination always same; size-dependent
  Exception: signed multiplication does allow for slightly different operation
Easiest way to evaluate instructions: figure out decimal values of operands, do operation in decimal, then figure out binary/hex values of results

## Slide 12: MUL/IMUL
MUL S  unsigned multiplication
IMUL S  signed multiplication
Byte: (AX) = (AL) * (S)
Word: (DX,AX) = (AX) * (S)
Double-word: (EDX,EAX) = (EAX) * (S)
Only CF, OF updated
  If upper half of result = 0, CF & OF = 0
  Otherwise, CF & OF = 1

## Slide 13: DIV/IDIV
DIV S  unsigned division
IDIV S  signed division
Result split into quotient, remainder
Byte: (AL) = (AX) / (S)
(AH) = (AX) % (S)
Word: (AX) = (DX,AX) / (S)
(DX) = (DX,AX) % (S)
Dword: (EAX) = (EDX,EAX) / (S)
(EDX) = (EDX,EAX) % (S)
Special “convert” instructions used to sign-extend value in register A before division
Flags undefined
  Overflow causes exception

## Slide 14: Example
Given
  EAX = 00000005h
  EBX = 0000FF02h
What are the results of the following instructions? (Assume all instructions start with same values in registers above)
  MUL BL
  MUL BH
  IMUL BH
  DIV BL
  DIV BH
  IDIV BH

## Slide 15: Solution
Consider that BH = FFh = 1111 11112
  As unsigned value, FFh = 25510
  As signed value, FFh = -110
MUL BL
  AX = AL * BL = 05h * 02h = 5 * 2 = 1010 = 000Ah
MUL BH
  Unsigned multiplication
  AX = AL * BH = 05h * FFh = 5 * 255 = 127510
  = 04FBh
IMUL BH
  Signed multiplication
  AX = AL * BH = 05h * FFh = 5 * -1 = -510 = FFFBh

## Slide 16: Solution (continued)
Consider that BH = FFh = 1111 11112
  As unsigned value, FFh = 25510
  As signed value, FFh = -110
DIV BL
  AL = AX / BL = 0005h / 02h = 5 / 2 = 02h
  AH = AX % BL = 0005h % 02h = 5 % 2 = 01h
DIV BH
  Unsigned division
  AL = AX / BH = 0005h / FFh = 5 / 255 = 00h
  AH = AX % BH = 0005h / FFh = 5 % 255 = 05h
IDIV BH
  Signed division
  AL = AX / BH = 0005h / FFh = 5 / -1 = -5 = FBh
  AH = AX % BH = 0005h % FFh = 5 % -1 = 00h

## Slide 17: Final notes
Next time:
  Logical, shift, and rotate instructions
Reminders:
  HW 1 due 1:00 PM today
  HW 2 to be posted; due 1:00 PM, 5/23