## Slide 1: 16.317 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2015
Lecture 17
HLL  assembly (continued)

## Slide 2: Lecture outline
Announcements/reminders
  HW 3 due 10/19
Review: HLL  assembly
  Static data
  Stack usage with function calls
Today’s lecture
  Conditional statements
  Loops

## Slide 3: Review: HLL  assembly
Global variables  static; allocated in data segment
Other variables  dynamic; allocated on stack
Stack frame for each function contains (from top)
  Saved variables within function
  Local variables for function (starting at EBP – 4)
  Saved EBP
  Saved EIP
  Function arguments (starting at EBP + 8)

## Slide 4: Stack accesses
On function call
SP or ESP: points to current top of stack
  Lowest address in current stack frame
BP or EBP: used to reference data within frame
  Arguments
  Local variables

## Slide 5: Stack accesses (cont.)
Arguments start at offset 8 from EBP
Local variables start at offset -4 from EBP
Starting offset of each variable can be defined as symbol
Ex. (testfile1.asm) _j$ = -120; size = 4
_i$ = -108; size = 4
_Y$ = -96; size = 40
_X$ = -48; size = 40
mov DWORD PTR _i$[ebp], 0
 sets i = 0

## Slide 6: Array accesses
To access array element, need
  Base address of array
  Offset into array
    Offset = index * (size of each element)
    For example, X[2] is 2*4 = 8 bytes into array X
In some ISAs, need to explicitly calculate this address
  Multiply index by element size
  Add to base address
x86 uses scaled addressing  multiplication done in memory access
  Example: code for X[i] = i * 2 from testfile1:
  mov eax, DWORD PTR _i$[ebp]
  shl eax, 1
  mov ecx, DWORD PTR _i$[ebp]
  mov DWORD PTR _X$[ebp+ecx*4], eax

## Slide 7: Conditional statements
If-then-else statements typically take form similar to:
<code to evaluate condition>
<conditional jump to else if false>
<code if condition true>
jmp end
else: <code if condition false>
end: …
<code to evaluate condition>
  Always requires a conditional branch
  Must add label to branch to “else” statement
Once statement for “if” condition is complete, jump past “else” statement
    Requires insertion of another label for jump target

## Slide 8: Conditional statements (cont.)
Body of inner loop:
if (j < 5)
Y[j] = X[i] + j;
else
Y[j] = X[i] – j;
cmp DWORD PTR _j$[ebp], 5
jge SHORT $LN2@main
mov eax, DWORD PTR _i$[ebp]
mov ecx, DWORD PTR _X$[ebp+eax*4]
add ecx, DWORD PTR _j$[ebp]
mov edx, DWORD PTR _j$[ebp]
mov DWORD PTR _Y$[ebp+edx*4], ecx
jmp SHORT $LN1@main
$LN2@main:
mov eax, DWORD PTR _i$[ebp]
mov ecx, DWORD PTR _X$[ebp+eax*4]
sub ecx, DWORD PTR _j$[ebp]
mov edx, DWORD PTR _j$[ebp]
mov DWORD PTR _Y$[ebp+edx*4], ecx
$LN1@main:

## Slide 9: Loops
Essentially three parts
  Initializing loop index
  Checking boundary condition
    Similar idea to if-then-else statements, but simpler
    If condition is false, end of loop
      Branch to label at first instruction after loop
    Usually done at start of loop, since no iterations should occur unless condition is true
      End of loop then contains jump back to beginning
  Incrementing loop index

## Slide 10: Loops (cont.)
for (j = 0; j < 10; j++) {// inner loop
mov DWORD PTR _j$[ebp], 0
jmp SHORT $LN5@main
$LN4@main:
mov eax, DWORD PTR _j$[ebp]
add eax, 1
mov DWORD PTR _j$[ebp], eax
$LN5@main:
cmp DWORD PTR _j$[ebp], 10
jge SHORT $LN3@main ; jmp to end
.
. ; Loop body here
.
jmp SHORT $LN4@main
$LN3@main:

## Slide 11: Final notes
Next time:
  HLL  assembly examples
Reminders:
  HW 3 to be posted; due 3/11