## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2016
Lecture 11:
Exam 1 Preview

## Slide 2: Lecture outline
Announcements/reminders
  HW 3 due today by 2:00 PM
    No late submissions—solution to be posted today
  Exam 1: Friday, 9/30
    Will be allowed calculator, one 8.5” x 11” double-sided note sheet
    x86 instructions covered through Monday are posted
Today’s lecture: Exam 1 Preview
  General exam notes
  Review of material

## Slide 3: Exam 1 notes
Allowed
  One 8.5” x 11” double-sided sheet of notes
  Calculator
x86 instruction set (so far) provided for you
No other notes or electronic devices (phone, laptop, etc.)
Exam will be 50 minutes
  Will start at 8:00 AM—please be on time!
Covers all lectures through Monday
General format
  1 multiple choice question
  2-3 short answer questions
  1 extra credit problem

## Slide 4: Test policies
Prior to passing out exam, I will verify that you only have one note sheet
  If you have multiple sheets, I will take all notes
You will not be allowed to remove anything from your bag after that point in time
  If you need an additional pencil, eraser, or piece of scrap paper during the exam, ask me
Only one person will be allowed to use the bathroom at a time
  You must leave your cell phone either with me or clearly visible on the table near your seat

## Slide 5: Review: ISA, storage
Instruction set architecture (cont.)
  Operands: the data being operated on
    How are the bits interpreted? (int, FP, signed/unsigned)
    What size are they? (byte, word, etc.)
    How do we reference operands?
Data storage
  Registers
    Small, fast set of on-chip storage (primarily for speed)
    Referenced by name
  Memory
    Larger, slower set of storage (primarily for capacity)
    Organized as hierarchy …
    … but programmer references single range of addresses
    Memory issues
      Aligned data: address divisible by number of bytes
      Endianness: 80x86 data is little endian

## Slide 6: Review: data & data transfer instructions
x86 data
  Registers: access as 8-bit (e.g. AL, AH), 16-bit (AX), 32-bit (EAX)
  Memory
    Data size usually matches register
    If not, explicitly specify (BYTE PTR, WORD PTR, DWORD PTR)
MOV: basic data transfer
  Can use registers, memory, immediates
MOVSX/MOVZX
  Sign-extend or zero-extend register/memory value
XCHG
  Exchange contents of source, dest

## Slide 7: Review: data transfer, arithmetic
LEA: load effective address
  Calculate EA/store in register
Reviewed flags: CF, AF, SF, ZF, PF, OF
Addition instructions
  ADD AX,BX  AX = AX + BX
  ADC AX,BX  AX = AX + BX + CF
  INC AX  AX = AX + 1
Subtraction instructions
  SUB AX,BX  AX = AX – BX
  SBB AX,BX  AX = AX – BX – CF
  DEC AX  AX = AX – 1
  NEG AX  AX = -AX = 0 - AX

## Slide 8: Review: Multiplication & division
Multiplication instructions
  MUL (unsigned), IMUL (signed)
  Result uses 2x bits of source
  Source usually implied (AL/AX/EAX)
Division instructions
  DIV (unsigned), IDIV (signed)
  Implied source (AX, (DX,AX), (EDX,EAX)) 2x bits of specified source
  Quotient/remainder split across result

## Slide 9: Review: Logical instructions
Logical instructions (AND/OR/XOR/NOT)
Basic shift instructions
  Move value by <amt> bits; add 0s to left or right
  CF = last bit shifted out
  SHL <src>, <amt>: Move <src> to left
    SAL exactly the same
  SHR <src>, <amt>: Move <src> to right
Arithmetic right shift
  Move value right by <amt> bits
  Copy sign bit to fill remaining bits
  CF = last bit shifted out
  SAR <src>, <amt>

## Slide 10: Review: rotate instructions
Rotate instructions: bits that are shifted out one side are shifted back in other side
  ROL <src>, <amt> or ROR <src>, <amt>
  CF = last bit rotated
Rotate through carry instructions
  CF acts as “extra” bit that is part of value being rotated
  RCL <src>, <amt> or RCR <src>, <amt>

## Slide 11: Review: bit test/scan
Bit test instructions
  Check state of bit and store in CF
  Basic test (BT) leaves bit unchanged
  Can also set (BTS), clear (BTR), or complement bit (BTC)
Bit scan instructions
  Find first non-zero bit and store index in dest.
  Set ZF = 1 if source non-zero; ZF = 0 if source == 0
  BSF: scan right to left (LSB to MSB)
  BSR: scan left to right (MSB to LSB)

## Slide 12: Final notes
Next time:
  Exam 1—PLEASE BE ON TIME!!