## Slide 1: 16.317 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2015
Lecture 14:
Jump and loop instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 3 to be posted; due date TBD
Today’s lecture
  Jump instructions
  Loop instructions

## Slide 3: Jump instructions
Used to change flow of program
  Next instruction specified by operand
Two general types
  Unconditional: JMP <target>
    Always goes to address indicated by <target>
  Conditional: Jcc <target>
    Jump only occurs if condition true
    cc replaced by valid condition code
      Most codes discussed in previous lecture
      Additional codes: CXZ/ECXZ
       CX/ECX register is zero

## Slide 4: Jump Instructions

## Slide 5: Example: program structure 1
Given the instructions below, what are the resulting register values if:
  AX = 0010H, BX = 0010H
  AX = 1234H, BX = 4321H
What type of high-level program structure does this sequence demonstrate?
Instructions
  CMP AX, BX
  JE L1
  ADD AX, 1
  JMP L2
  L1: SUB AX, 1
  L2: MOV [100H], AX

## Slide 6: Example solution
First case: AX = BX = 0010H
  CMP AX, BX  Shows AX == BX
  JE L1  Cond. true—jump to L1
  ADD AX, 1
  JMP L2
  L1: SUB AX, 1  AX = AX – 1 = 000F
  L2: MOV [100H], AX  Store 000F at DS:100H

## Slide 7: Example solution (cont.)
Second case: AX = 1234H, BX = 4321H
  CMP AX, BX  Shows AX < BX
  JE L1  Cond. false—no jump
  ADD AX, 1  AX = AX + 1 = 1235H
  JMP L2
  L1: SUB AX, 1  AX = AX – 1 = 000F
  L2: MOV [100H], AX  Store 000F at DS:100H

## Slide 8: Example solution (cont.)
High-level program structure: if/else statement
  If part: compare + jump (if (AX == BX))
  Else part: what follows if condition false
  Unconditional jump used to skip “if” part
  Both parts have same exit (L2)

## Slide 9: Example: program structure 2
Given the instructions below, what are the resulting register values if, initially, AX = 0001H?
What type of high-level program structure does this sequence demonstrate?
Instructions
  MOV CL, 5
  L: SHL AX, 1
  DEC CL
  JNZ L

## Slide 10: Example: program structure 3
Given the instructions below, what are the resulting register values if, initially, AX = 0001H?
What type of high-level program structure does this sequence demonstrate?
Instructions
  MOV CX, 5
  L: JCXZ END
  ADD AX, AX
  DEC CX
  JMP L
  END: MOV [10H], AX

## Slide 11: Block Move Program

## Slide 12: Loop instructions
Common operations in basic loops
  Compare
  Conditional jump
  Decrement loop counter (CX)
Loop instructions combine all into one op
  All decrement CX by 1, then check if CX == 0
  <target> must be short-label (8-bit immediate)
  LOOP <target>: Return to <target> if CX != 0
  LOOPE/LOOPZ <target>: Return to <target> if (CX != 0) && (ZF == 1)
  LOOPNE/LOOPNZ <target>: Return to <target> if (CX != 0) && (ZF != 1)

## Slide 13: Loop Program Structure
Structure of a loop
  CX = initial count
  Loop body: code to be repeated
  Loop instruction– determines if loop is complete or if the body is to repeat
Example: block move

## Slide 14: Loop example 1
Rewrite the post-tested loop seen earlier using a loop instruction:
  MOV CL, 5
  L: SHL AX, 1
  DEC CL
  JNZ L
Solution:
  MOV CL, 5
  L: SHL AX, 1
  LOOP L

## Slide 15: Loop example 2
Describe the operation of the following program (Example 6.15-6.16).
What is the final value of ESI if the 15 bytes between 0A001 and 0A00F have the following values?
  00 01 02 03 04 05 06 07 08 09 0A 0B 0C 0D 0E
MOV DL, 05
MOV EAX, 0000A000h
MOV ESI, 00000000h
MOV CX, 000F
AGAIN:INC SI
CMP [EAX + ESI], DL
LOOPNE AGAIN

## Slide 16: Final notes
Next time:
  Subroutines
Reminders:
  HW 3 to be posted; due date TBD