## Slide 1: 16.317 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2015
Lecture 5:
Assembly basics
Data transfer instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 1 due 2:00 PM, 9/18
Today’s lecture
  Assembly basics
  Data transfer instructions

## Slide 3: Review: x86 data types
Refresher on x86 registers
  Gen. purpose registers: 16 or 32 bits
  Data registers can hold 8 bit data as well
  Determining size: register name
  Example: “accumulator” register
    8 bit data: AL = lowest byte; AH = next lowest byte
    16 bit data: AX = lowest 16 bits (AH/AL together as word)
    32 bit data: EAX = entire 32 bits
Say EAX = 1A2B3C4DH
  What are AL, AH, and AX?
  AL = 4DH, AH = 3CH, AX = 3C4DH

## Slide 4: Instruction Assembly Notation
Each instruction is represented by a mnemonic that describes its operation—called its operation code (opcode)
  MOV = move (data transfer)
  ADD = add (arithmetic)
  AND = logical AND (logic)
  JMP = unconditional jump (control transfer)
Operands are the other parts of an assembly language instructions
    Identify whether the elements of data to be processed are in registers or memory
      Source operand– location of one operand to be processed
      Destination operand—location of the other operand to be processed and the location of the result

## Slide 5: Assembly Language Statements
General structure of an assembly language statement
LABEL: INSTRUCTION ;COMMENT
  Label—address identifier for the statement
  Instruction—the operation to be performed
  Comment—documents the purpose of the statement
  Example:
START: MOV AX, BX ; Copy BX into AX
Other examples:
  INC SI ;Update pointer
ADD AX, BX
  Few instructions have a label—usually marks a jump to point
  Not all instructions need a comment

## Slide 6: x86 memory accesses
# bytes from memory usually = # bytes in register
Example: MOV AX, [100H]
  AX is 16-bit register  move word from address 100H to AX
Sometimes necessary to specify size
  Use “<size> PTR”: BYTE PTR, WORD PTR, DWORD PTR
  Example: MOVZX EAX, BYTE PTR [100H]
    Take byte from memory
    Zero-extend data to 32 bits and store in EAX
Remember, x86 uses little-endian data

## Slide 7: Data transfer instructions
MOV
MOVSX
MOVZX
XCHG
LEA
Load full pointer
Additional data transfer instructions (covered later, if at all)
  PUSH/POP (stack transfers)
  INS/OUTS (I/O)
  MOVS/LODS/STOS (string instructions)
  BSWAP (switch from little endian to big endian)
  XLAT (table lookup)
  CMOV (conditional move)

## Slide 8: MOV
Used to copy data between
  Registers
  Registers/memory
  Immediate value (source only) to register/memory
Format: MOV D, S
Operation: (D) = (S)
Restrictions
  Immediate value can only be used as source
  If segment register is destination, source must be memory or register (no immediate)

## Slide 9: MOV examples
Assume: AX = 0100H, CS = 3000H,
(100H) = 00H, (101H) = FFH
MOV BL, AL
  BL = AL = 00H
MOV DX, CS
  DX = CS = 3000H
MOV CX, [100H]
  CX = word starting at 100H = FF00H

## Slide 10: Usage of Move Instruction
Example—Initialization of internal registers with immediate data and address information
  What is the final state of all affected registers?
  Why is AX used to initialize segment registers?

## Slide 11: Usage of Move Instruction (soln)
MOV AX, 2000H  AX = 2000H
MOV DS, AX  DS = AX = 2000H
MOV ES, AX  ES = AX = 2000H
MOV AX, 3000H  AX = 3000H
MOV SS, AX  SS = 3000H
MOV AX, 0H  AX = 0000H
MOV BX, AX  BX = AX = 0000H
MOV CX, 0AH  CX = 000AH
MOV DX, 100H  DX = 0100H
MOV SI, 200H  SI = 0200H
MOV DI, 300H  DI = 0300H

## Slide 12: MOVSX/MOVZX
Move and extend data (fill upper bits with 0/1)
  ZX  zero extend
  SX  sign extend  copy MSB of source
Format: MOVZX D, S
MOVSX D, S
Operation: lower bits of D = S
upper bits of D = 0 (MOVZX) or
upper bits of D = MSB of S (MOVSX)
Restrictions
  Only register/memory operands (no immediates)
  Source must contain fewer bits than destination
  If memory operand used, size must be specified

## Slide 13: MOVSX/MOVZX examples
Assume: AX = 0100H, DX = 8100H,
(100H) = 00H, (101H) = FFH
What are the results of the following instructions?
MOVSX EBX, AX
MOVSX EBX, DX
MOVZX EBX, DX
MOVSX EBX, BYTE PTR [100H]
MOVSX EBX, WORD PTR [100H]

## Slide 14: MOVSX/MOVZX examples (soln)
Assume: AX = 0100H, DX = 8100H, (100H) = 00H, (101H) = FFH
What are the results of the following instructions?
MOVSX EBX, AX
  EBX = AX sign-extended = 00000100H (orig. value underlined)
MOVSX EBX, DX
  EBX = DX sign-extended = FFFF8100H
MOVZX EBX, DX
  EBX = DX zero-extended = 00008100H
MOVSX EBX, BYTE PTR [100H]
  EBX = byte at 100h sign-extended = 00000000H
MOVSX EBX, WORD PTR [100H]
  EBX = word at 100h sign-extended = FFFFFF00H

## Slide 15: Final notes
Next time:
  Finish data transfer instructions
  Arithmetic instructions
Reminders:
  HW 1 due 2:00 PM, 9/18