## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Summer 2016
Lecture 2:
x86 intro
Assembly basics
Data transfer instructions

## Slide 2: Lecture outline
Announcements/reminders
  Sign up for the course discussion group on Piazza
  HW 1 due 1:00 PM, 5/19
    Bring hard copies to class or leave in envelope on office door
    E-mail electronic submissions to Dr. Geiger
      Please attach only a single file (archives not accepted)
      Include your name in some way in the file name (i.e., mgeiger_hw1.docx)
  Exam 3: 6/23 instead of 6/27
Review
  Data types
  Alignment and endianness
Today’s lecture
  Addressing modes
  x86 introduction
  x86 memory accesses

## Slide 3: Review: ISA, storage
Instruction set architecture (cont.)
  Operands: the data being operated on
    How are the bits interpreted? (int, FP, signed/unsigned)
    What size are they? (byte, word, etc.)
    How do we reference operands?
Data storage
  Registers
    Small, fast set of on-chip storage (primarily for speed)
    Referenced by name
  Memory
    Larger, slower set of storage (primarily for capacity)
    Organized as hierarchy …
    … but programmer references single range of addresses
    Memory issues
      Aligned data: address divisible by number of bytes
      Endianness: 80x86 data is little endian

## Slide 4: Addressing modes
Addressing modes: ways of specifying operand location
Where are operands stored? (3 location types)
  Registers  register addressing
    Provide name of register; value read from register
  Memory
    Provide address in memory; value read from that location
    Several modes for specifying memory address
  In the instruction  immediate addressing

## Slide 5: Memory addressing
Instructions accessing memory generate effective address (EA)
  Address calculated as part of instruction
  EA can be used as
    Actual memory address in a simple memory system
    Address within a particular segment in a segmented memory architecture
Effective address calculations can involve
  A constant value
  One or more values stored in registers
  Some combination of register and constant

## Slide 6: General memory addressing modes
Memory direct addressing
  EA = constant value encoded in instruction
Register indirect addressing
  EA = value stored in register
Base + displacement addressing
  EA = constant displacement + base register(s)
  Can have variations of this mode based on number and type of registers
Scaled addressing
  EA = base + (scale * index)
  Used for array addressing

## Slide 7: x86 intro
“x86”  family of general purpose Intel processors
  Starts with 8086 processor (1978)
  Used (w/extensions) in current processors
Supports use of 8, 16, 32, or 64 bit data
  “IA-32”: x86 for 32-bit processors (80386 and later)
  “x86-64”: x86 with 64-bit extensions (AMD, Intel, VIA)
  “IA-64”: old name for Itanium server architecture (not extension of x86)
Allows both register and memory operands
Segmented or flat memory architecture
Real and protected mode operation
  Protected mode supports virtual memory

## Slide 8: Register Set
Nine 32-bit registers
  Data registers- EAX, EBX, ECX, EDX, can be used as 32, 16 or 8bit
  Pointer registers- EBP, ESP
  Index registers- ESI, EDI
  Instruction pointer- EIP (not shown)
Flags (status) register-EFLAGS (not shown)
Source: http://www.cs.virginia.edu/~evans/
cs216/guides/x86.html

## Slide 9: Register Set
64-bit extensions added with Pentium 4
  Data/pointer/index/IP/ flag register extended to 64 bits
  For example:
    RAX = 64-bit register A
    RSP = 64-bit stack pointer
  8 additional data registers (R8-R15)

## Slide 10: General Purpose Data Registers
Four general purpose data registers
  Accumulator (A) register
  Base (B) register
  Count (C) register
  Data (D) register
Can hold 8-bit, 16-bit, or 32-bit data
  AH/AL = high and low byte value
  AX = word value
  EAX = double word value
General uses:
  Hold data such as source or destination operands for most operations—ADD, AND, SHL
  Hold address pointers for accessing memory
Some also have dedicated special uses
  C—count for loop,
  B—table look-up translations, base address
  D—indirect I/O and string I/O

## Slide 11: Pointer/Index Registers
Two pointer registers (32-/16-bit versions)
  Stack pointer register (ESP/SP)
    Points to top of stack
  Base pointer register (EBP/BP)
    Points to fixed location within current stack frame
Two index registers
  Source index (ESI/SI)
  Destination index (EDI/DI)
  Typically used in memory addressing

## Slide 12: Flags Register
32-bit register holding single bit status and control information
9 active flags in real mode
Two categories
  Status flags: conditions resulting from instruction
    Most instructions update status
    Used as test conditions
  Control flags: control processor functions
    Used by software to turn on/off operating capabilities

## Slide 13: x86 memory spaces
x86 architecture implements independent memory and input/output (not shown) address spaces
Memory address space
  1 MB “real” memory
    System + transient program area (TPA)
  Extended memory size dependent on processor
Input/output address space- 65,536 bytes long (64KB)

## Slide 14: x86 memory modes
Two general modes of access
  Real mode (DOS)
  Protected mode (Windows)
Two memory models
  Segmented memory model
  Flat memory model
    We’ll use this model

## Slide 15: Flat mode addressing
No segmentation
  Entire address space active
Address generated by instruction = linear address being accessed
Generates 40-bit external address

## Slide 16: x86 addressing modes
Addresses in x86 instructions enclosed by brackets
Addressing modes: all examples of general addressing modes discussed earlier
Direct addressing
  EA = constant value
  Example: MOV AX, [0100H]
Register indirect addressing
  EA = value stored in register
  Example: MOV [EDI], AX
Base-plus-index addressing
  EA = sum of two registers
  Example: MOV AX, [EBX+ESI]

## Slide 17: x86 addressing modes (cont.)
Register relative addressing
  EA = register + constant
  Examples:
    MOV CL, [EBX+4]
    MOV AX, ARRAY[EBX] ARRAY is constant memory location
Base relative-plus-index addressing
  EA = base register + index register + constant
  Example: MOV AX, 10H[ESI][EBX] -or-
  MOV AX, [10H+SI+BX]
Scaled-index addressing
  EA = register + (scaling factor * second register)
  Often useful for array accesses
    Scaling factor = element size (2, 4, 8 bytes)
  Example: MOV EDX, [EAX + 4*EBX]

## Slide 18: Example
Compute the address for the memory operand in each of the following instructions.
  You do not need to specify what data is transferred
The register contents and variables are as follows:
  (ESI) = 0000010016
  (EDI) = 0000020016
  (EBX) = 0000030016
MOV [EBX+0400h], CX
MOV [EDI+2*EBX], AH
MOV [EBX+EDI+0400h], AL

## Slide 19: Example solutions
Memory operand in: MOV [EBX+0400h], CX
  Addr = value in EBX + 0400h
  = 00000300h + 0400h = 00000700h
Memory operand in: MOV [EDI+2*EBX], AH
  Addr = value in EDI + 2 * value in EBX
  = 00000200h + 2 * 00000300h
  = 00000200h + 00000600h
Memory operand in MOV [EBX+EDI+0400h], AL
  Addr = EBX + EDI + 0400h
  = 00000300H + 00000200H + 0400h = 00000900h

## Slide 20: Instruction Assembly Notation
Each instruction is represented by a mnemonic that describes its operation—called its operation code (opcode)
  MOV = move (data transfer)
  ADD = add (arithmetic)
  AND = logical AND (logic)
  JMP = unconditional jump (control transfer)
Operands are the other parts of an assembly language instructions
    Identify whether the elements of data to be processed are in registers or memory
      Source operand– location of one operand to be processed
      Destination operand—location of the other operand to be processed and the location of the result

## Slide 21: Assembly Language Statements
General structure of an assembly language statement
LABEL: INSTRUCTION ;COMMENT
  Label—address identifier for the statement
  Instruction—the operation to be performed
  Comment—documents the purpose of the statement
  Example:
START: MOV AX, BX ; Copy BX into AX
Other examples:
  INC SI ;Update pointer
ADD AX, BX
  Few instructions have a label—usually marks a jump to point
  Not all instructions need a comment

## Slide 22: x86 memory accesses
# bytes from memory usually = # bytes in register
Example: MOV AX, [100H]
  AX is 16-bit register  move word from address 100H to AX
Sometimes necessary to specify size
  Use “<size> PTR”: BYTE PTR, WORD PTR, DWORD PTR
  Example: MOVZX EAX, BYTE PTR [100H]
    Take byte from memory
    Zero-extend data to 32 bits and store in EAX
Remember, x86 uses little-endian data

## Slide 23: Data transfer instructions
MOV
MOVSX
MOVZX
XCHG
LEA
Load full pointer
Additional data transfer instructions (covered later, if at all)
  PUSH/POP (stack transfers)
  INS/OUTS (I/O)
  MOVS/LODS/STOS (string instructions)
  BSWAP (switch from little endian to big endian)
  XLAT (table lookup)
  CMOV (conditional move)

## Slide 24: MOV
Used to copy data between
  Registers
  Registers/memory
  Immediate value (source only) to register/memory
Format: MOV D, S
Operation: (D) = (S)
Restrictions
  Immediate value can only be used as source
  If segment register is destination, source must be memory or register (no immediate)

## Slide 25: MOV examples
Assume: AX = 0100H, CS = 3000H,
(100H) = 00H, (101H) = FFH
MOV BL, AL
  BL = AL = 00H
MOV DX, CS
  DX = CS = 3000H
MOV CX, [100H]
  CX = word starting at 100H = FF00H

## Slide 26: Usage of Move Instruction
Example—Initialization of internal registers with immediate data and address information
  What is the final state of all affected registers?
  Why is AX used to initialize segment registers?

## Slide 27: Usage of Move Instruction (soln)
MOV AX, 2000H  AX = 2000H
MOV DS, AX  DS = AX = 2000H
MOV ES, AX  ES = AX = 2000H
MOV AX, 3000H  AX = 3000H
MOV SS, AX  SS = 3000H
MOV AX, 0H  AX = 0000H
MOV BX, AX  BX = AX = 0000H
MOV CX, 0AH  CX = 000AH
MOV DX, 100H  DX = 0100H
MOV SI, 200H  SI = 0200H
MOV DI, 300H  DI = 0300H

## Slide 28: MOVSX/MOVZX
Move and extend data (fill upper bits with 0/1)
  ZX  zero extend
  SX  sign extend  copy MSB of source
Format: MOVZX D, S
MOVSX D, S
Operation: lower bits of D = S
upper bits of D = 0 (MOVZX) or
upper bits of D = MSB of S (MOVSX)
Restrictions
  Only register/memory operands (no immediates)
  Source must contain fewer bits than destination
  If memory operand used, size must be specified

## Slide 29: MOVSX/MOVZX examples
Assume: AX = 0100H, DX = 8100H,
(100H) = 00H, (101H) = FFH
What are the results of the following instructions?
MOVSX EBX, AX
MOVSX EBX, DX
MOVZX EBX, DX
MOVSX EBX, BYTE PTR [100H]
MOVSX EBX, WORD PTR [100H]

## Slide 30: MOVSX/MOVZX examples (soln)
Assume: AX = 0100H, DX = 8100H, (100H) = 00H, (101H) = FFH
What are the results of the following instructions?
MOVSX EBX, AX
  EBX = AX sign-extended = 00000100H (orig. value underlined)
MOVSX EBX, DX
  EBX = DX sign-extended = FFFF8100H
MOVZX EBX, DX
  EBX = DX zero-extended = 00008100H
MOVSX EBX, BYTE PTR [100H]
  EBX = byte at 100h sign-extended = 00000000H
MOVSX EBX, WORD PTR [100H]
  EBX = word at 100h sign-extended = FFFFFF00H

## Slide 31: XCHG
Swap contents of source and destination
Format: XCHG D, S
Operation: (D) = (S)
(S) = (D)
Restrictions:
  Memory operand can only be used as destination

## Slide 32: LEA
Perform effective address computation and store result in register
Format: LEA D, EA
Operation: D = EA
Example: LEA SI, [10H + DI]

## Slide 33: Example
 | Lo |  |  | Hi
0x528000 | 50 | 88 | 31 | A3
0x528004 | B2 | FF | 0F | 7D
0x528008 | 07 | D0 | BE | 22
0x52800C | 11 | 96 | 00 | 14
Given the initial memory contents at left, show the results of the following instruction sequence:
MOV EAX, 528000h
MOV EBX, [EAX+2]
XCHG BL, BH
LEA EDX, [EAX+8]
MOV ECX, [EDX-3]

## Slide 34: Solution
MOV EAX, 528000h
EAX = 528000h
MOV EBX, [EAX+2]
EBX = DWORD at 528002h = FFB2A331h
XCHG BL, BH
Swap BL and BH  EBX = FFB231A3h
LEA EDX, [EAX+8]
EDX = EAX+8 = 528008h
MOV ECX, [EDX-3]
ECX = DWORD at 528005h = 077D0FFFh

## Slide 35: Final notes
Next time:
  Arithmetic instructions
Reminders:
  Sign up for the course discussion group on Piazza
  HW 1 due 1:00 PM, 5/19
    Bring hard copies to class or leave in envelope on office door
    E-mail electronic submissions to Dr. Geiger
      Please attach only a single file (archives not accepted)
      Include your name in some way in the file name (i.e., mgeiger_hw1.docx)
  Exam 3: 6/23 instead of 6/27