## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Spring 2016
Lecture 22:
PIC instruction set (continued)

## Slide 2: Lecture outline
Announcements/reminders
  HW 6 due 1:00 PM, 3/28
    No late submissions
  Exam 2 in class Wednesday, 3/30
    Covers material through today
    Instruction list to be posted
    Allowed one double-sided 8.5” x 11” note sheet; calculator
  PICkits to be handed out soon
    Will have to work in groups (3 students preferred size)
Review
  Multi-bit manipulation
  Shift/rotate
Today’s lecture
  Continue with PIC instruction set

## Slide 3: Review: Multi-bit Manipulation
Examples:
andlw B’00000111’ ;force upper 5 bits of W to zero
andwf TEMP1, F ;TEMP1 <- TEMP1 AND W
andwf TEMP1, W ;W <- TEMP1 AND W
iorlw B’00000111’ ;force lower 3 bits of W to one
iorwf TEMP1, F ;TEMP1 <- TEMP1 OR W
xorlw B’00000111’ ;complement lower 3 bits of W
xorwf TEMP1, W ;W <- TEMP1 XOR W
andlw k ; AND literal value k into W
andwf f, F(W) ; AND W with f, putting result in F or W
iorlw k ; Inclusive-OR literal value k into W
iorwf f, F(W) ; Inclusive-OR W with f, putting result in F or W
xorlw k ; Exclusive-OR literal value k into W
xorwf f, F(W) ; Exclusive-OR W with f, putting result in F or W
STATUS bits:
Z

## Slide 4: Review: Shift/Rotate
asrf f, F(W) ; copy f into F or W; shift F or W right one bit, keeping
; sign intact; shift LSB into C
lsrf f, F(W) ; copy f into F or W; shift F or W right one bit, shifting
; 0 into MSB; shift LSB into C
lslf f, F(W) ; copy f into F or W; shift F or W left one bit, shifting
; 0 into LSB; shift MSB into C
rlf f, F(W) ; copy f into F or W; rotate F or W left through
; the carry bit
rrf f, F(W) ; copy f into F or W; rotate F or W right through
; the carry bit
STATUS bits:
C

## Slide 5: Example
Show the values of all changed registers after the following sequence
Assume the carry bit is initially 0
cblock 0x40
z
endc
clrf z
movlw 0xF0
iorwf z, F
xorlw 0xFF
rrf z, F
andwf z, W
lslf z, F
asrf z, F

## Slide 6: Example solution
clrf z  z = 0
movlw 0xF0  W = 0xF0
iorwf z, F  z = z OR W = 0xF0
xorlw 0xFF  W = W XOR 0xFF
= 0xF0 XOR 0xFF
= 0x0F
rrf z, F  Rotate z right thru carry
Before rotate, (z, carry) = 1111 0000 02
 z = 0111 10002 = 0x78, C = 0
andwf z, W  W = z AND W
= 0x78 AND 0x0F = 0x08
lslf z, F  Shift z left
Before shift, z = 0111 10002
 z = 1111 00002 = 0xF0, C = 0
asrf z, F  Arithmetic shift right
z = 1111 10002 = 0xF8, C = 0

## Slide 7: Control flow
Examples:
goto There ; Next instruction to be executed is labeled “There”
call Task1 ; Push return address; Next instruction to be
; executed is labeled “Task1”
return ; Pop return address off of stack
retlw 5 ; Pop return address; W <- 5
retfie ; Pop return address; re-enable interrupts
goto label ; Go to labeled instruction
bra label ; Go to labeled instruction
brw ; Relative branch using W as offset
call label ; Call labeled subroutine
callw ; Subroutine call using W as address
return ; Return from subroutine
retlw k ; Return from subroutine, putting literal
; value in W
retfie ; Return from interrupt service routine;
; re-enable interrupts
STATUS bits:
none

## Slide 8: Conditional Execution
Examples:
btfsc TEMP1, 0 ; Skip the next instruction if bit 0 of TEMP1 equals 0
btfss STATUS, C ; Skip the next instruction if C==1
decfsz TEMP1, F ; Decrement TEMP1, skip if TEMP1==0
incfsz TEMP1, W ; W <- TEMP1+1 , skip if W==0 (TEMP1==0xFF)
; Leave TEMP1 unchanged
btfsc f, b ;Test bit b of register f, where b=0 to 7, skip if clear
btfss f, b ;Test bit b of register f, where b=0 to 7, skip if set
decfsz f, F(W) ;decrement f, putting result in F or W, skip if zero
incfsz f, F(W) ;increment f, putting result in F or W, skip if zero
STATUS bits:
none
Conditional execution in PIC: skip next instruction if condition true
Two general forms
  Test bit and skip if bit clear/set
  Increment/decrement register and skip if result is 0

## Slide 9: Example
Show the values of all changed registers after each of the following sequences
  What high-level operation does each perform?
(a) movf a, W
sublw 0x1A
btfsc STATUS, Z
goto L1
incf b, W
goto L2
L1
decf b, W
L2
movwf a
(b) movf NUM2, W
subwf NUM1, W
btfss STATUS, C
goto BL
movf NUM1, W
goto Done
BL
movf NUM2, W
Done
movwf MAX

## Slide 10: Example solution (part a)
movf a, W  W = a
sublw 0x1A  W = 0x1A – a
btfsc STATUS, Z  Skip goto if result
is non-zero
goto L1  Goto L1 if result == 0
 Reach this point if
result non-zero
incf b, W  W = b + 1
goto L2
L1
decf b, W  W = b - 1
L2
movwf a  a = W  value depends
on what’s executed before this
High-level operation:
if (a == 0x1A)
a = b – 1
else
a = b + 1

## Slide 11: Example solution (part b)
movf NUM2, W  W = NUM2
subwf NUM1, W  W = NUM1 – W
= NUM1 – NUM2
btfss STATUS, C  Carry indicates borrow of 0
 if set, NUM1 >= NUM2
goto BL
movf NUM1, W  if (NUM1 >= NUM2)
W = NUM1
goto Done  Skip “below” section
BL
movf NUM2, W  if (NUM1 < NUM2)
W = NUM2
Done
movwf MAX
High-level operation:
if (NUM1 >= NUM2)
MAX = NUM1
else
MAX = NUM2

## Slide 12: Final notes
Next time:
  PIC programming
Reminders:
  HW 6 due 1:00 PM, 3/28
    No late submissions
  Exam 2 in class Wednesday, 3/30
    Covers material through today
    Instruction list to be posted
    Allowed one double-sided 8.5” x 11” note sheet; calculator
  PICkits to be handed out soon
    Will have to work in groups (3 students preferred size)