## Slide 1: 16.317 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2015
Lecture 7:
Arithmetic instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 1 due 2:00 PM today
  HW 2 to be posted; due 2:00 PM, 9/25
Review
  Data transfer instructions (XCHG, LEA)
Today’s lecture
  Arithmetic instructions

## Slide 3: Flags
All arithmetic instructions set flags
  CF = carry flag (carry output from MSB of add/sub)
  OF = overflow flag
  ZF = zero flag (result is zero)
  SF = sign flag (1 if negative, 0 if positive)
  PF = parity flag (even parity in LSB)
  AF = auxiliary carry (carry between nibbles)
Stored in FLAGS register
Referenced in conditional instructions

## Slide 4: Addition instructions
ADD D, S
  Operation: (D) = (D) + (S)
ADC D, S
  Operation: (D) = (D) + (S) + (CF)
INC D
  Operation: (D) = (D) + 1

## Slide 5: Subtraction instructions
SUB D, S
  Operation: (D) = (D) – (S)
SBB D, S
  Operation: (D) = (D) – (S) – (CF)
DEC D
  Operation: (D) = (D) – 1
NEG D
  Operation: (D) = -(D)
  Two’s complement negation

## Slide 6: Addition/subtraction examples
Given the following initial state:
  AX = 1234H
  BL = ABH
  Memory location SUM = 00CDH
Show the results of each step of the following instruction sequence:
  ADD AX, [SUM]
  ADC BL, 05H
  NEG BL
  SUB AX, 12H
  INC WORD PTR [SUM]

## Slide 7: Example solution
ADD AX, [SUM]
  (AX) = (DS:SUM) + (AX)
  00CDH + 1234H = 1301H
  (AX) = 1301H, (CF) = 0
ADC BL,05H
  (BL) = (BL) + IMM8 +(CF)
  ABH + 05H + 0 = B0H
  (BL) = B0H, (CF) = 0
NEG BL
  (BL) = –(BL)
  –B0H = –(1011 0000)2 = 0101 00002 = 50H

## Slide 8: Example solution (cont.)
SUB AX, 12H
  (AX) = (AX) – 0012H
  1301H – 0012H = 12EFH
  (AX) = 12EFH, (CF) = 0
INC WORD PTR [SUM]
  (DS:SUM) = (DS:SUM) + 1
  00CDH + 1 = 00CEH
  (SUM) = 00CEH, (CF) = 0

## Slide 9: Final notes
Next time:
  Multiplication and division
  Logical and shift instructions
Reminders:
  HW 1 due 2:00 PM today
  HW 2 to be posted; due 2:00 PM, 9/25