## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Spring 2016
Lecture 21:
PIC instruction set (continued)

## Slide 2: Lecture outline
Announcements/reminders
  HW 5 due 2:30 PM today
  HW 6 to be posted; due 1:00 PM, 3/28
    No late submissions
  Exam 2 in class Wednesday, 3/30
    Instruction list to be posted
    Allowed one double-sided 8.5” x 11” note sheet; calculator
  PICkits to be handed out soon
    Will have to work in groups (3 students preferred size)
Review
  PIC instruction set basics
  Data transfers
  Bit manipulation instructions
Today’s lecture
  Arithmetic instructions
  Logical instructions
  Shift/rotate instructions

## Slide 3: Review: PIC instructions
Four typical instruction formats (+ few special purpose)
  Upper bits of all hold opcode
  Byte-oriented includes 1 bit destination, 7 bit direct address
  Bit-oriented includes 3 bit position (0-7), 7 bit direct address
  Literal/control includes 8 bit literal
  CALL/GOTO includes 11 bit literal
Variable declarations
  cblock <start_address>: start of variable declarations
  All names between cblock/endc directives assigned to consecutive bytes starting at <start_address>

## Slide 6: Review: PIC instructions (cont.)
Clearing register: clrw/clrf
Moving values: movlw/movwf/movf
Swap nibbles: swapf
Single bit manipulation: bsf/bcf

## Slide 7: Increment/Decrement/ Complement
Examples:
incf TEMP1, F ;Increment TEMP1
incf TEMP1, W ;W <- TEMP1+1; TEMP1 unchanged
decf TEMP1, F ;Decrement TEMP1
comf TEMP1, F ;Change 0s and 1s to 1s and 0s
incf f, F(W) ; increment f, putting result in F or W
decf f, F(W) ;decrement f, putting result in F or W
comf f, F(W) ;complement f, putting result in F or W
STATUS bits:
Z

## Slide 8: Addition/Subtraction
Examples:
addlw 5 ; W = 5+W
addwf TEMP1, F ; TEMP1 = TEMP1+W
sublw 5 ; W = 5-W (not W = W-5 )
subwf TEMP1, F ; TEMP1 = TEMP1 - W
addlw k ;add literal value k into W
addwf f, F(W) ;add w and f, putting result in F or W
addwfc f, F(W) ;add w, f, and C, putting result in F or W
sublw k ;subtract W from literal value k, putting
;result in W
subwf f, F(W) ;subtract W from f, putting result in F or W
subwfb f, F(W) ;subtract f – W – (~C), putting result in F or W
STATUS bits:
C, DC, Z

## Slide 9: Example
Show the values of all changed registers after the following sequence
cblock 0x20
varA
varB
varC
endc
clrf varA
clrf varB
clrf varC
incf varA, W
sublw 0x0F
addwf varB, F
decf varB, F
comf varB, W
subwf varC, F

## Slide 10: Example solution
clrf varA  varA = 0
clrf varB  varB = 0
clrf varC  varC = 0
incf varA, W  W = varA + 1 = 1
sublw 0x0F  W = 0x0F – W = 0x0F – 1
= 0x0E
addwf varB, F  varB = varB + W = 0x0E
decf varB, F  varB = varB – 1 = 0x0D
comf varB, W  W= ~varB = ~0x0D = 0xF2
subwf varC, F  varC = varC – W = 0x0E

## Slide 11: Multi-bit Manipulation
Examples:
andlw B’00000111’ ;force upper 5 bits of W to zero
andwf TEMP1, F ;TEMP1 <- TEMP1 AND W
andwf TEMP1, W ;W <- TEMP1 AND W
iorlw B’00000111’ ;force lower 3 bits of W to one
iorwf TEMP1, F ;TEMP1 <- TEMP1 OR W
xorlw B’00000111’ ;complement lower 3 bits of W
xorwf TEMP1, W ;W <- TEMP1 XOR W
andlw k ; AND literal value k into W
andwf f, F(W) ; AND W with f, putting result in F or W
iorlw k ; Inclusive-OR literal value k into W
iorwf f, F(W) ; Inclusive-OR W with f, putting result in F or W
xorlw k ; Exclusive-OR literal value k into W
xorwf f, F(W) ; Exclusive-OR W with f, putting result in F or W
STATUS bits:
Z

## Slide 12: Shift/Rotate
asrf f, F(W) ; copy f into F or W; shift F or W right one bit, keeping
; sign intact; shift LSB into C
lsrf f, F(W) ; copy f into F or W; shift F or W right one bit, shifting
; 0 into MSB; shift LSB into C
lslf f, F(W) ; copy f into F or W; shift F or W left one bit, shifting
; 0 into LSB; shift MSB into C
rlf f, F(W) ; copy f into F or W; rotate F or W left through
; the carry bit
rrf f, F(W) ; copy f into F or W; rotate F or W right through
; the carry bit
STATUS bits:
C

## Slide 13: Final notes
Next time:
  Continue with PIC instruction set
Reminders:
  HW 5 due 2:30 PM today
  HW 6 to be posted; due 1:00 PM, 3/28
    No late submissions
  Exam 2 in class Wednesday, 3/30
    Instruction list to be posted
    Allowed one double-sided 8.5” x 11” note sheet; calculator
  PICkits to be handed out soon
    Will have to work in groups (3 students preferred size)